## Slide 1: SeeForMe
AI COURSE FINAL PROJECT
A multimodal accessibility assistant that tells you when it isn’t sure
Goutham, [Member 2], [Member 3], [Member 4], [Member 5]
[Course name] · October 2026
Notes: Presenter: [Member 2]. Introduce the team and the one-line idea. SeeForMe lets a blind or low-vision person take or upload a photo, ask about it by typing or speaking, and hear the answer. What makes it different: it says “I’m not sure” out loud when it isn’t sure, and it refuses advice a photo can’t support. Paste the matching block from docs/presentation_script.md here.

## Slide 2: The problem and what the brief asked
People who can’t see need answers to their own questions:
Which medicine is this?
What does this sign say?
Is the stove on?
They can’t check the answer, so the AI must be honest about what it doesn’t know.
What the brief asked for
Upload a photo, then multi-turn visual Q&A
Spoken responses
An explicit low-confidence behavior
30-image test set: accuracy and cost of errors
Ethics: when should an AI refuse?
SeeForMe
Presenter: [Member 2]
2
Notes: Presenter: [Member 2]. Start with the three questions on the left: these are everyday questions a sighted person answers in a glance. The key point is the bold line: a blind user can’t check the answer, so a confident wrong answer is the worst outcome. On the right, the five things the brief asked for; every one maps to a module on the next slide.

## Slide 3: From the brief to five modules
WHAT THE BRIEF ASKED
MODULE
Multi-turn visual Q&A, frozen encoder plus connector
1
Vision-language core
Low-confidence behavior, when to refuse
2
Safety, ethics and confidence
Upload or capture, spoken responses
3
Accessible interface
Runs locally, without failures
4
Platform and performance
30-image test, accuracy and cost of errors
5
Evaluation and data
“The model proposes, our code decides.”
SeeForMe
Presenter: [Member 4]
3
Notes: Presenter: [Member 4]. Each row of the brief became one module with one owner. Read across a row or two: the brief asked for a low-confidence behavior, so Module 2 owns safety, ethics and confidence. Land the footnote: the model proposes, our code decides. That idea shapes the architecture on the next slide.

## Slide 4: Architecture: the model proposes, code decides
Module 3
Photo
Camera, upload, paste
Module 4
Quality check
OpenCV blur and brightness
Module 1
Vision-language model
Qwen2.5-VL 3B via Ollama
Module 2
Safety rules
Plain code that refuses, hedges, flags
Module 3
Answer
Sentence, confidence, voice
Module 4: FastAPI server and browser page. Sessions in memory only. One question at a time.
Module 5: runs the same pipeline over a frozen test set and scores it.
SeeForMe
Presenter: Goutham
4
Notes: Presenter: Goutham. Walk left to right: a photo comes in, a quality check catches blur and darkness before the model sees it, the vision-language model proposes an answer, and the safety rules decide what is actually said. The amber box is the main design decision. Safety is ordinary code after the model, so it can be tested and the model cannot talk its way past it. Module 4 hosts everything; Module 5 runs the same pipeline over a frozen test set.

## Slide 5: Module 1: the vision-language core
Qwen2.5-VL 3B runs locally through Ollama, about 3 GB
The photo goes in once; follow-ups reuse it, so a second answer takes seconds
Answers are forced into a JSON shape: answer, confidence, category, reason, retake flag
The prompt asks for full spoken sentences and only what is readable
Vision encoder
frozen
Connector
image → tokens
Language model
writes the answer
~1,100
image tokens per photo
Course tie-in
Frozen vision encoder, connecting layer and language model, as in Flamingo.
SeeForMe
Presenter: Goutham
5
Notes: Presenter: Goutham. The core is Qwen2.5-VL 3B, a small vision-language model that runs on the laptop through Ollama, about 3 GB. Each photo becomes roughly 1,100 image tokens, which is where most of the time goes. The photo goes in once and follow-up questions reuse it, so a second answer takes seconds. Every answer is forced into a JSON shape so our code can read the confidence and category. The design matches what we studied in class: a frozen vision encoder, a connecting layer and a language model, as in Flamingo.

## Slide 6: Module 2: safety, ethics and confidence
Refuse
Advice a photo can’t support, such as doses or “is it safe to take”. We read what is printed and point to a pharmacist.
Hedge
Low confidence starts with “I’m not sure” plus a next step. A stove is never reported as surely off. A blurry photo can’t give high confidence.
Ignore
Instructions written inside a photo are data, not commands.
The rules are plain code that runs after the model, so they can be tested. They can only raise the risk, never lower it.
SeeForMe
Presenter: [Member 3]
6
Notes: Presenter: [Member 3]. Three behaviours. Refuse: when the question needs advice a photo can’t support, like a dose, we read what is printed and point to a pharmacist. Hedge: low confidence is said out loud, starting with “I’m not sure”, always with a next step; a stove is never reported as surely off, and a blurry photo can’t produce high confidence. Ignore: text inside a photo is treated as data, never as a command. These rules are ordinary code after the model, so we can test them, and they can only raise the risk level, never lower it.

## Slide 7: Module 3: the accessible interface
Photo from a file, paste, drag and drop, or the live camera
The camera speaks guidance (too dark, hold steady, move closer) and takes the photo when it is sharp
Spoken answers with replay, and a microphone to speak the question
Keyboard-only use, screen-reader mode, high-contrast theme, large text
TBD
TBD: screenshot of the app with an answer card visible
SeeForMe
Presenter: [Member 4]
7
Notes: Presenter: [Member 4]. A photo can come from a file, a paste, drag and drop, or the live camera. The camera talks the user into a good photo: too dark, hold steady, move closer, and it takes the shot itself once the picture is sharp. Answers are spoken, with replay, and the question can be spoken too. Everything works from the keyboard, with a screen-reader mode, a high-contrast theme and large text. Point to the screenshot to show a real answer card.

## Slide 8: Module 4: platform and performance
FastAPI server: sessions in memory, upload limits, one question at a time
A photo-quality check runs before the model
Runs entirely on a MacBook Air M1 with 8 GB
Speed depends on free memory
Seconds per answer (measured)
Memory starved
135 s
Chrome open
71 s
Chrome closed
30 s
Memory free
9 s
On a small machine, free memory beats code changes.
SeeForMe
Presenter: [Member 5]
8
Notes: Presenter: [Member 5]. The server is FastAPI: sessions live in memory only, uploads are limited, and it handles one question at a time. A photo-quality check runs before the model so bad photos never cost a model call. Everything runs on a MacBook Air M1 with 8 GB. The chart is the key finding: the same question took 135 seconds when memory was starved, 71 with Chrome open, 30 with Chrome closed, and 9 with memory free. On a small machine, free memory beats code changes.

## Slide 9: Module 5: evaluation and results
TBD
of 30 test items handled correctly
TBD
confident wrong answers on high-risk items
TBD
seconds typical per answer
Test set mix (30 items)
Signage
8
Hazard
6
Document
5
Medication
4
Label
4
Unanswerable
3
How we tested
30 test items, run once
12 separate items for tuning
Cost: a confident wrong medicine answer = 20, a hedged miss on a low-risk item = 1
Every grade checked against the photo
SeeForMe
Presenter: [Member 2]
10
Notes: Presenter: [Member 2]. The three headline numbers are still to be filled in from the locked test run: items handled correctly out of 30, confident wrong answers on high-risk items, and typical seconds per answer. The test set has 30 items across six kinds, and we tuned only on 12 separate items so we couldn’t overfit the test. Errors are weighted by cost: a confident wrong medicine answer costs 20, a hedged miss on a low-risk item costs 1. Every grade was checked by a person against the photo.

## Slide 10: Failures we found and what we learned
Invented meaning
Read a blurry Startup Repair screen as a password prompt, with high confidence.
Fix: describe only what is readable.
Cache leak
One photo’s content showed up in the next photo’s answer.
Fix: a separate id for each conversation.
Gate too strict
Blocked a readable braille photo as blurry.
Lesson: flat textures fool a sharpness test.
Grader error
My grader marked a correct answer wrong and faked a safety alarm.
Fix: a person now checks every grade.
TBD
TBD: top failure patterns from the test set
SeeForMe
Presenter: Goutham
11
Notes: Presenter: Goutham. Four failures, each with what we changed. Invented meaning: the model read a blurry Startup Repair screen as a password prompt, with high confidence; the prompt now asks it to describe only what is readable. Cache leak: one photo’s content showed up in the next photo’s answer; each conversation now gets its own id. Gate too strict: a readable braille photo was blocked as blurry, because flat textures fool a sharpness test; this is a documented trade-off. Grader error: my own grader marked a correct answer wrong and raised a false safety alarm, so a person now checks every grade. The test-set failure patterns will be added after the locked run.

## Slide 11: Ethics, limits and what comes next
When should an AI refuse?
When a photo can’t support the answer and a wrong answer is dangerous
Always with a next step, never just “no”
Limits
A small model that is sometimes confidently wrong
Rules that keywords can miss
What comes next
A bigger hosted model
Local speech recognition
Testing with real users
Few-shot style examples
TBD: result
Thank you. Questions?
[GitHub link] · VizWiz data (CC BY 4.0) · Qwen2.5-VL via Ollama
SeeForMe
Presenter: [Member 3], then everyone
12
Notes: Presenter: [Member 3], everyone joins for the thanks. Our answer to the brief’s ethics question: an AI should refuse when a photo can’t support the answer and a wrong answer could be dangerous, and it should always offer a next step rather than a bare “no”. Be honest about limits: a small model is sometimes confidently wrong, and keyword rules can miss cases. Next: a bigger hosted model, local speech recognition, testing with real blind and low-vision users, and few-shot examples (result to be added). Thank the audience and open for questions.

## Slide 12: Live demo
1
Medicine bottle: reads the label and adds a verify line
2
“How many tablets should I take?” Refused, rule shown
3
Blurry photo: asks for a retake
4
Camera: spoken guidance, then auto-capture
5
Handwritten “ignore instructions” note: not obeyed
TBD
TBD: app screenshot
SeeForMe
[Member 5] narrates · [Member 4] drives
9
Notes: [Member 5] narrates, [Member 4] drives. 1: Medicine bottle: it reads the label and adds a line asking the user to verify. 2: Ask “How many tablets should I take?”: it refuses and shows the rule that fired. 3: A blurry photo: it asks for a retake instead of guessing. 4: The live camera: listen for the spoken guidance, then the automatic capture. 5: A handwritten note saying “ignore instructions”: the assistant reads it as text and does not obey it. Backup plan if the live demo fails: [add recorded video or screenshots].